Position(Real)
stepPosition(Integer)
cycleTime
Time

---
Initial condition
”scale” is known = steps/mm
initialPosition
initialStepPosition

---
End condition
commandedPosition - 3 examples here

---
StepPosition for end
commandedPosition - 3 examples here
stepPosition =
       floor(commandedPosition*scale)

---
Check for no step
if initialStepPosition == stepPosition
take no step
goto update and return success
commandedPosition
stepPosition

---
Check for too many steps
too high frequency
commandedPosition
stepPosition
commandedPosition
stepPosition
approximateFrequency = abs(initialStepPosition - commandedStepPosition)/cycleTime
if approximateFrequency > maxAllowedFrequency
take no step
goto update and return error

---
Line equations
intitialStepPosition != stepPosition
frequency slow enough
commandedPosition
commandedStepPosition
stepPos = k Time + m
k = (commandedPosition - initialPosition)/cycleTime
m = initialPosition
Time = 0 at initial Time (nominal lcnc time)

---
intitialStepPosition != stepPosition, must take step
frequency slow enough
Check for too flat slope
commandedPosition
stepPosition
Avoid problems with numerical precision at flat slope.
k * cycleTime * scale = amount of a step to take
if that amount < 0.01 (for example), just take a step in the
right direction half-way into cycleTime.
We know we must take a step due to previous checks.

---
intitialStepPosition != stepPosition, must take step
frequency range ok
Tstart
Tstart
For positive k:
Tstart = ((InitialStepPosition+1)/scale - m)/k
For negative k:
Tstart = (InitialStepPosition/scale - m)/k
Tstart

---
intitialStepPosition != stepPosition, must take step
frequency range ok
Tstart is known
Frequency
Tstart
Frequency = slope of curve, k * scale
Frequency = k * scale
Tstart

---
intitialStepPosition != stepPosition, must take step
Frequency range ok
Tstart is known
Frequency is known
Number of steps
and direction
commandedPosition
commandedStepPosition
Tstart
nSteps = commandedStepPosition - initialStepPosition
sign(nSteps) = direction
sign(k) = direction
Tstart
commandedPosition
stepPosition

---
Prepare for next cycle
initialPosition <= commandedPosition
initialStepPosition <= commandedStepPosition

---
Pulses
Tstart
T=1/frequency
Tstart
Tstart
Tstart
Tstart

---
Note. Time scale is different in this and following slides
Pulses
Pulse train is defined by
Tstart + Tjitter
frequency
nSteps
T=0 is measured from SM2 interrupt, which seems to happen within 2-3 μsecs
Therefor, Tjitter = 5 μsecs
Tjitter
Tstart
Tstart
T=1/frequency
Tstart
Tjitter
Tjitter
Tstart
Tstart
Tstart

---
Note. Time scale is different in this and following slides
Starting the pulse train
Use HardwareTimer (stm32duino)
Take one of the 1-channel timers 10,11,13,14 on STM32F4 (AN4013)
startTimer->attachInterrupt(startTimerCB); // At constructor time
startTimer->setOverflow(Tjitter+Tstart, MICROSEC_FORMAT); // Now
startTimer->ressume(); //
Let the timer run for Tjitter+Tstart usecs, then it calls startTimerCB (below)
pulseTimer->setMode(pulseTimerChan, TIMER_OUTPUT_COMPARE_PWM2, stepPin);
pulseTimer->setOverflow(uint32_t(frequency), HERTZ_FORMAT);
pulseTimer->setCaptureCompare(pulseTimerChan, 50, PERCENT_COMPARE_FORMAT); // 50%
pulseTimerSteps = abs(nSteps);
pulseTimer->resume();
// Use local copy of nSteps, so it doesn’t accidentally gets overwritten.
Tjitter
Tstart
Tstart
T=1/frequency
Tstart
Tjitter
Tjitter
Tstart
Tstart
Tstart

---
Note. Time scale is different in this and following slides
Ending the pulse train
PulseTimer runs and calls pulseTimerCB at end of every PWM pulse
Number of steps to do are counted down and when 0, stop the pulseTimer
--timerPulseSteps;
if (timerPulseSteps == 0)
     pulseTimer->pause();
Tjitter
Tstart
Tstart
T=1/frequency
Tstart
Tjitter
Tjitter
Tstart
Tstart
Tstart

---
Problem with this approach

---
The end is unpredictable and collides with next step’s pwm train
Tstart can be predicted accurately
The end of the pulse train also, Tend = Tstart + nStep / frequency
A problem occurs when Tstart,2 happens before Tend (Tstart,2 = Tstart for the next cycle)
At Tstart and Tstart,2 the pwm timer is reloaded. If that happens before the pwm pulse train is finished, problems occur.
At constant speed, every 1 ms we see a part of an overall long pulse train, just take a 1 ms piece and make pulses.
That’s what this procedure does. This works generally fine at constant speed, I think.
At increased and decreased speed, during acceleration, Tstart,2 is not what one think at first. It will be shorter or longer
and the situation described above occurs, when the pwm timer gets reloaded before it is finished.
The rising edge of the pwm pulse is in the right place, but everything that comes may not be.
It can not be like that.
Tend
Tjitter
Tstart,2
Tstart
Tstart
T=1/frequency
Tjitter
Tjitter
Tstart
Tstart
Tstart

---
Remedies
1. Skip Tstart and distribute pulses inside cycleTime window, keeping clear of the start and end
2. Modify pulse shape to use the most narrow pulse allowed by the driver
3. Don’t check for complete pulse at period update, but on capture/compare.
4. Keep frequency as before
5. Use end time of previous pulse when setting the time for the first pulse
Not perfect.
It will often happen that there are n and n+1 pulses in adjacent cycles. This will result in frequency jumping up and down.
2.5+2.5 usec => 5 usec and max 200 kHz. I don’t need that much. Say 5+5 usecs => max 100 kHz.
Tjitter
T=1/frequency
Interrupt here