Position(Real)
stepPosition(Integer)
cycleTime
Time

---
Initial condition
”scale” is known = steps/mm
initialPosition
initialStepPosition

---
End condition
commandedPosition - 3 examples here

---
StepPosition for end
commandedPosition - 3 examples here
stepPosition =
       floor(commandedPosition*scale)

---
Check for no step
if initialStepPosition == stepPosition
take no step
goto update and return success
commandedPosition
stepPosition

---
Check for too many steps
too high frequency
commandedPosition
stepPosition
commandedPosition
stepPosition
approximateFrequency = abs(initialStepPosition - commandedStepPosition)/cycleTime
if approximateFrequency > maxAllowedFrequency
take no step
goto update and return error

---
Line equations
intitialStepPosition != stepPosition
frequency slow enough
commandedPosition
commandedStepPosition
stepPos = k Time + m
k = (commandedPosition - initialPosition)/cycleTime
m = initialPosition
Time = 0 at initial Time (nominal lcnc time)

---
intitialStepPosition != stepPosition, must take step
frequency slow enough
Check for too flat slope
commandedPosition
stepPosition
Avoid problems with numerical precision at flat slope.
k * cycleTime * scale = amount of a step to take
if that amount < 0.01 (for example), just take a step in the
right direction half-way into cycleTime.
We know we must take a step due to previous checks.

---
intitialStepPosition != stepPosition, must take step
frequency range ok
Tstart
Tstart
For positive k:
Tstart = (ceil(initialPosition*scale)-m)/k
For negative k:
Tstart = -(floor(initialPosition*scale)-m)/k
Tstart

---
intitialStepPosition != stepPosition, must take step
frequency range ok
Tstart is known
Frequency
Tstart
Frequency = slope of curve, k * scale
Frequency = k * scale
Tstart

---
intitialStepPosition != stepPosition, must take step
Frequency range ok
Tstart is known
Frequency is known
Number of steps
and direction
commandedPosition
commandedStepPosition
Tstart
nSteps = commandedStepPosition - initialStepPosition
sign(nSteps) = direction
sign(k) = direction
Tstart
commandedPosition
stepPosition

---
Prepare for next cycle
initialPosition <= commandedPosition
initialStepPosition <= commandedStepPosition

---
Pulses
Tstart
T=1/frequency
Tstart
Tstart
Tstart
Tstart

---
Note. Time scale is different in this and following slides
Pulses
Pulse train is defined by
Tstart + Tjitter
frequency
nSteps
T=0 is measured from SM2 interrupt, which seems to happen within 2-3 μsecs
Therefor, Tjitter = 5 μsecs
Tjitter
Tstart
Tstart
T=1/frequency
Tstart
Tjitter
Tjitter
Tstart
Tstart
Tstart

---
Note. Time scale is different in this and following slides
Starting the pulse train
Use HardwareTimer (stm32duino)
Take one of the 1-channel timers 10,11,13,14 on STM32F4 (AN4013)
startTimer->attachInterrupt(startTimerCB); // At constructor time
startTimer->setOverflow(Tjitter+Tstart, MICROSEC_FORMAT); // Now
startTimer->ressume(); //
Let the timer run for Tjitter+Tstart usecs, then it calls startTimerCB (below)
pulseTimer->setMode(pulseTimerChan, TIMER_OUTPUT_COMPARE_PWM2, stepPin);
pulseTimer->setOverflow(uint32_t(frequency), HERTZ_FORMAT);
pulseTimer->setCaptureCompare(pulseTimerChan, 50, PERCENT_COMPARE_FORMAT); // 50%
pulseTimerSteps = abs(nSteps);
pulseTimer->resume();
// Use local copy of nSteps, so it doesn’t accidentally gets overwritten.
Tjitter
Tstart
Tstart
T=1/frequency
Tstart
Tjitter
Tjitter
Tstart
Tstart
Tstart

---
Note. Time scale is different in this and following slides
Ending the pulse train
PulseTimer runs and calls pulseTimerCB at end of every PWM pulse
Number of steps to do are counted down and when 0, stop the pulseTimer
--timerPulseSteps;
if (timerPulseSteps == 0)
     pulseTimer->pause();
Tjitter
Tstart
Tstart
T=1/frequency
Tstart
Tjitter
Tjitter
Tstart
Tstart
Tstart